## Slide 1: Well engineering and P&A Standards
Ing. Peter Hudec

## Slide 2
1 NAFTA WELL ENGINEERING
2 P&A STANDARDS
3 CONCLUSIONS AND RECOMMMENDATIONS
AGENDA

## Slide 3: 1
NAFTA WELL ENGINEERING

## Slide 4
  COMPETENCE CENTRE
  Nafta has own competence center and prepare and provide:
  Workover, P&A Drilling and well intervention organizing and supervising
  Well integrity management
  Mining rescue services
  Slickline/wireline services
  Laboratory
  Consultancy
NAFTA well engineering
Coiled Tubing

## Slide 5
  Nafta has 2 own crews and rigs for P&A/Workover/Drilling:
P&A 2021:
  NAFTA group: 3 wells (SK)
  Ext. Companies: 4 wells (D)
  Ext. Companies: 4 wells (CZ) re-abandonment
  Workover 2021:
  NAFTA group: 24 wells (SK)
  Ext. Companies: 13 wells (CZ)
P&A in Germany 2021-2022:
  NAFTA abandoned wells 4 in 2021 and 4 wells in 2022
  Wells has integrity issues and on most of them were milled out casings.
  The presence of NAFTA engineers on the well helped to solving many issues during the P&A process.
P&A / Workover
RIGS:
GVS 3070 70t
MR 4000 90t
BIR 8000 140t
MR 4000

## Slide 6
structure
facilities
NAFTA / Mining RESCUE services
15 professional rescuers
65 voluntary rescuers
Training centre with training well
Special equipment
Athey wagon
2 Pumps 20 m3/min
6“ hoses – 2 500 m
Firefighting equipment
self-contained breathing apparatus (SCBA)
Measuring instruments
Training well which allows simulate blowout and well control operations
Training room for intervention in unbreathable environment

## Slide 7
Structure and facilities
Services
NAFTA / wireline and slickline services
2 operating crews
2 slickline/wireline trucks
Slickline operation
Downhole dynamic pressure and temperature measuring, online production tests
Downhole memory B&W camera
Spinner downhole measuring, flow profile of completions and producing zones
CCL, Thermometry
Downhole samples
Setting / Pulling plugs, Shifting sliding sleeves
Sand bailing
Acoustic and temperature measuring with GESO

## Slide 8
Structure and facilities
Services
NAFTA / Laboratory services
1 head of laboratory
5 laboratory technician
Isotopic composition of hydrocarbons
Gas composition of hydrocarbons
Water and HC Dew Point measuring
HC Dew Point calculations
Water Content Calculations
High/Low pressure gas samples
Calorific Calculations
Isotopic analyser
Chromatograph

## Slide 9: 2
P&A STANDARDS

## Slide 10
SLOVAK REPUBLIC
The Slovak Republic legislation does not specify exactly how to P&A wells. NAFTA submits to the Slovak Mining Authority a plan for the P&A and the Mining Authority makes a statement. NAFTA have internal standard for P&A wells.
CZECH REPUBLIC
The P&A process is determined by Ordinance No. 239/1998 Coll. § 71b.
GERMANY
The P&A process is determined by Guideline of the Mining Authority in Clausthal-Zellerfeld
UK
The P&A process is determined by Guidelines for the Abandonment of Wells (Oil & Gas UK)
P&A Standards – Nafta Group

## Slide 11
Revision of general conditions of the well before P&A
  Head of cement behind the casing
  Well integrity issues (Sustain Casing Pressure, Casing corrosion, ...)
  Hydrocarbon saturated horizons
  Hydrocarbon saturated horizons with H2S or CO2
P&A Standards - NAFTA
Possible ways of gas migration
UGS horizon
Ways of gas
Way of gas
Impermeable barriers in both horizontal and vertical directions.

## Slide 12
P&A Standards - NAFTA
Isolation through perforation
Open-hole isolation
Isolation through perforation
Isolation above perforation (in case of impassable perforation)
Open-hole isolation
Lier head/cut casing head isolation
Cement bridge plug
Cement bridge plug
Cement bridge plug
Cement bridge plug
Mechanical bridge plug
Cement retainer
Cement bridge plug
Mechanical bridge plug
Mechanical bridge plug
Cement bridge plug
Cement bridge plug
Cement bridge plug
Cement bridge plug
Drilling mud
Liner head or Casing head
Mechanical bridge plug
Cement bridge plug

## Slide 13
P&A Standards - NAFTA
The casing strings are cut and welded 2m under surface with concreate block on top.
Mechanical plug and 50m of cement bridge plug.
Good cement in annulus confirmed by CBL and VDL logging
Mechanical plug and 50m of cement bridge plug.
Cement plug squeezed to perforation
The casing strings are cut and welded 2m under surface with concreate block on top.
Mechanical plug and 50m of cement bridge plug.
Mechanical plug and 60m of cement bridge plug.
Good cement in annulus confirmed by CBL and VDL logging
Mechanical plug and 50m of cement bridge plug.
Cement plug squeezed to perforation

## Slide 14
P&A Standards - NAFTA
30 m of milled and underreamed section with cement bridge plug or 30m of DYNASLOT perforation with squeezed resin
Gas migration behind the casing
The casing strings are cut and welded 2m under surface with concreate block on top.
Mechanical plug and 50m of cement bridge plug.
Mechanical plug and 60m of cement bridge plug.
Mechanical plug and 50m of cement bridge plug.
Good cement in annulus confirmed by CBL and VDL logging
Mechanical plug and 50m of cement bridge plug.
Cement plug squeezed to perforation

## Slide 15: 3
CONCLUSIONS AND RECOMMMENDATIONS

## Slide 16
KEY POINTS
  Individual approach
  Well history
  Current well integrity status
  Special temperature and ultrasound logging
  P&A standards knowledge
  Know how
  Observing and monitoring well area after P&A
Conclusions and recommendations

## Slide 17: Contact
Ing. Peter Hudec
Head of Subsurface dept
Tel: +421 917 728 058
Email: peter.hudec@nafta.sk