## Slide 1: Gas Balance model

## Slide 2
Sources | History (before 3/2023) | Forecast assumptions (3-12/2023)
Demand | Eurostat (until 12/2022) | 5/10/15% reduction vs 2017-21
Flows | ENTSOG, Eustream | RU flows as YTD, others as 2022
LNG | GIE | 2022 plus 0-10bcm y-o-y (IEA, Shell)
Production | Eurostat (until 12/2022) | 2022 minus 5bcm y-o-y (UK, NL)
Storage inj. | GIE | Residual
(Im)balance | Residual = 1.1 % (model validation) | 0
OUR APPROACH
The model focuses on Europe as depicted on the map
Starting point: gas storages as of 1 Apr 2023
Demand is the most uncertain parameter especially in connection with development of gas prices
LNG imports as secondary parameter in sensitivity analysis

## Slide 3
EU target: 15% consumption reduction vs. 2017-2021 avg. for Aug22-Mar23
For countries within our scope 18% reduction has been made for Aug22-Feb23 (and 11% for 2022), partly due to favourable weather
Reduction differed by segments. Split of 13% reduction 2022 vs 2021 (‘OECD Europe‘ - IEA):
  Households 15% (~190 bcm)
  Industry 20% (~180 bcm)
  Gas to Power 4% (~130 bcm)
We assume 10% YTG reduction (12% for full 2023: 421bcm)
  Households demand will recover slightly (weather impact) but not before the next heating season starts
  Gas to Power demand will decrease due to expanding renewables combined with nuclear base effect
  Industry uncertain
DEMAND
YTG demand reduction (vs. 2017-2021)
Chart: Consumption mcm/d
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2017-2021 range | 2213.2645 | 2110.2286 | 1764.0581 | 1453.8335 | 1065.8527 | 868.8343 | 928.4578 | 863.2126 | 979.3433 | 1249.6322 | 1714.9333 | 1883.471
min | 1816.3548 | 1787.7933 | 1435.771 | 1011.4291 | 860.6129 | 839.8467 | 813.3921 | 762.0524 | 899.1982 | 1157.2154 | 1590.4773 | 1723.0548
2022 | 1939.8382 | 1710.8924 | 1534.9963 | 1188.7999 | 853.0637 | 798.7407 | 789.4593 | 720.2524 | 832.8509 | 907.7764 | 1267.7971 | 1611.9074
2023 (Jan+Feb act., YTG modelled) | 1539.8877 | 1593.384 | 1429.9164 | 1085.3152 | 874.9508 | 771.4614 | 782.2221 | 739.2669 | 855.1473 | 1082.457 | 1491.9818 | 1638.8288
2017-2021 avg. | 2031.4967 | 1892.1102 | 1584.8571 | 1203.3037 | 970.849 | 856.1178 | 868.1981 | 820.4531 | 948.8583 | 1200.807 | 1653.7707 | 1815.7866
Chart: Consumption in bcm
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023F
Hist. consumption | 484706.9 | 472238.2 | 486492.061 | 469983.378 | 491111.845 | 429626.75
AVG -15% | 402559.6154
AVG -10% | 18247.5497
AVG -5% | 18247.5497
 | 484706.9 | 472238.2 | 486492.061 | 469983.378 | 491111.845 | 429626.75 | 439054.7148
AVG 2017-21 | 480906.4768 | 480906.4768 | 480906.4768 | 480906.4768 | 480906.4768 | 480906.4768 | 480906.4768

## Slide 4
Price vs demand reduction
Lower demand destruction to be expected in the summer due to y-o-y gas price decrease
Chart: Gas price (€/MWh) vs. demand reduction (%)
| 44565 | 44566 | 44567 | 44568 | 44571 | 44572 | 44573 | 44574 | 44575 | 44578 | 44579 | 44580 | 44581 | 44582 | 44585 | 44586 | 44587 | 44588 | 44589 | 44592 | 44593 | 44594 | 44595 | 44596 | 44599 | 44600 | 44601 | 44602 | 44603 | 44606 | 44607 | 44608 | 44609 | 44610 | 44613 | 44614 | 44615 | 44616 | 44617 | 44620 | 44621 | 44622 | 44623 | 44624 | 44627 | 44628 | 44629 | 44630 | 44631 | 44634 | 44635 | 44636 | 44637 | 44638 | 44641 | 44642 | 44643 | 44644 | 44645 | 44648 | 44649 | 44650 | 44651 | 44652 | 44655 | 44656 | 44657 | 44658 | 44659 | 44662 | 44663 | 44664 | 44665 | 44670 | 44671 | 44672 | 44673 | 44676 | 44677 | 44678 | 44679 | 44680 | 44684 | 44685 | 44686 | 44687 | 44690 | 44691 | 44692 | 44693 | 44694 | 44697 | 44698 | 44699 | 44700 | 44701 | 44704 | 44705 | 44706 | 44707 | 44708 | 44711 | 44712 | 44713 | 44718 | 44719 | 44720 | 44721 | 44722 | 44725 | 44726 | 44727 | 44728 | 44729 | 44732 | 44733 | 44734 | 44735 | 44736 | 44739 | 44740 | 44741 | 44742 | 44743 | 44746 | 44747 | 44748 | 44749 | 44750 | 44753 | 44754 | 44755 | 44756 | 44757 | 44760 | 44761 | 44762 | 44763 | 44764 | 44767 | 44768 | 44769 | 44770 | 44771 | 44774 | 44775 | 44776 | 44777 | 44778 | 44781 | 44782 | 44783 | 44784 | 44785 | 44788 | 44789 | 44790 | 44791 | 44792 | 44795 | 44796 | 44797 | 44798 | 44799 | 44803 | 44804 | 44805 | 44806 | 44809 | 44810 | 44811 | 44812 | 44813 | 44816 | 44817 | 44818 | 44819 | 44820 | 44823 | 44824 | 44825 | 44826 | 44827 | 44830 | 44831 | 44832 | 44833 | 44834 | 44837 | 44838 | 44839 | 44840 | 44841 | 44844 | 44845 | 44846 | 44847 | 44848 | 44851 | 44852 | 44853 | 44854 | 44855 | 44858 | 44859 | 44860 | 44861 | 44862 | 44865 | 44866 | 44867 | 44868 | 44869 | 44872 | 44873 | 44874 | 44875 | 44876 | 44879 | 44880 | 44881 | 44882 | 44883 | 44886 | 44887 | 44888 | 44889 | 44890 | 44893 | 44894 | 44895 | 44896 | 44897 | 44900 | 44901 | 44902 | 44903 | 44904 | 44907 | 44908 | 44909 | 44910 | 44911 | 44914 | 44915 | 44916 | 44917 | 44918 | 44923 | 44924 | 44925
2022 demand reduction % | -0.045119 | -0.095775 | -0.031461 | -0.012053 | -0.12132 | -0.06702 | -0.090692 | -0.12213 | -0.12226 | -0.24403 | -0.23339 | -0.11228
2023 demand reduction | -0.24199 | -0.15788

## Slide 5
Assumptions for 3/2023 - 12/2023:
Same as Jan-Feb 2023 (-46bcm y-o-y, of which -33bcm YTG)
2022 less delta Norwegian outages (-1.8bcm y-o-y, of which -1.5bcm YTG)
Same as 2022
Same as 2022
Pipeline flows + production
Assumptions for 2023
UK: North Sea Transition Authority forecast (-1.6bcm YTG)
NL: Dutch government forecast (-2.8bcm YTG)
RO: Same as 2022
OTH: Same as 2022
-3.4
Chart: Pipeline flows (mcm/d)
| 44562 | 44593 | 44621 | 44652 | 44682 | 44713 | 44743 | 44774 | 44805 | 44835 | 44866 | 44896 | 44927 | 44958 | 44986 | 45017 | 45047 | 45078 | 45108 | 45139 | 45170 | 45200 | 45231 | 45261
Azerbaijan to IT | 22.0687 | 23.6222 | 26.2231 | 27.7187 | 27.3323 | 28.5854 | 27.8746 | 25.3588 | 28.8528 | 28.0074 | 26.764 | 23.6273 | 24.1938 | 22.7922 | 26.2231 | 27.7187 | 27.3323 | 28.5854 | 27.8746 | 25.3588 | 28.8528 | 28.0074 | 26.764 | 23.6273
N.Africa | 93.5795 | 92.5464 | 92.2623 | 95.0614 | 90.1684 | 89.8081 | 83.0373 | 92.0759 | 98.4595 | 92.3501 | 88.6476 | 106.9867 | 72.5367 | 84.0292 | 92.2623 | 95.0614 | 90.1684 | 89.8081 | 83.0373 | 92.0759 | 98.4595 | 92.3501 | 88.6476 | 106.9867
Norway(+UK) | 320.7309 | 331.0841 | 318.3678 | 309.3924 | 308.6413 | 301.1032 | 318.0678 | 310.8519 | 271.4574 | 318.0944 | 302.8014 | 320.2674 | 320.8585 | 319.9396 | 314.7185 | 294.9454 | 239.8451 | 259.1822 | 339.762 | 282.2284 | 285.4337 | 332.9702 | 324.0347 | 357.9739
RU | 267.2434 | 313.4743 | 353.4269 | 301.478 | 275.7284 | 180.7529 | 133.2044 | 123.819 | 88.5304 | 74.0094 | 75.1524 | 89.5216 | 58.5375 | 67.6933 | 63.1154 | 63.1154 | 63.1154 | 63.1154 | 63.1154 | 63.1154 | 63.1154 | 63.1154 | 63.1154 | 63.1154
Chart: Production in bcm
| 2022 Act | 2023 FC
UK | 37.774 | 35.8968
Netherlands | 18.4018 | 14.9547
Romania | 9.138 | 9.138
Others | 18.5355 | 18.5355
-1.9

## Slide 6
LNG – Who takes the incremental supply?
LNG supply growth in 2023 will be around 23bcm (Freeport?)
Potential split to regions is presented in the chart on the right (Outlook by Shell)
IEA forecasts 10bcm increment for Europe
In 1-3/2023 imports to Europe already +3.4bcm y-o-y
Full year increase modelled in three scenarios:
Scenarios | Import in bcm | Increment in bcm | Narrative for 2023
2022 | 149.2 |  | 
Low case 2023 | 149,2 | + 0.0 | 2023 on the same level as 2022, i.e. YTG lower y-o-y
Base case 2023 | 154,2 | + 5.0 | +3.4bcm y-o-y in 1-3/2023, +0.2bcm every month between 4/2023-12/2023
High case 2023 | 159,2 | + 10.0 | In line with IEA forecast

## Slide 7
LNG sendout development
LNG high case arguments
China LNG imports in 1-2/2023 slightly below 2022
Europe YTD imports (as of March) already +3.4bcm above past year without any sign of decline
LNG low case arguments
Delay of Freeport restart
Potential outages during the year
Gas prices declined significantly in the last couple of months may attract demand from price sensitive regions
Chart: LNG sendout in bcm
| 44562 | 44593 | 44621 | 44652 | 44682 | 44713 | 44743 | 44774 | 44805 | 44835 | 44866 | 44896 | 44927 | 44958 | 44986 | 45017 | 45047 | 45078 | 45108 | 45139 | 45170 | 45200 | 45231 | 45261
Bel | 803.4366 | 664.0751 | 749.3897 | 1083.7183 | 805.9906 | 1059.0423 | 1167.108 | 935.4178 | 778.7042 | 1070.1221 | 1131.9531 | 1130.3286 | 1101.0892 | 949.7934 | 1136.4969
Fra | 3151.0329 | 2470.6385 | 3077.8592 | 3124.9859 | 3112.4601 | 1738.7981 | 2821.5775 | 3043.0235 | 2546.4413 | 2760.7981 | 3290.1033 | 3493.5305 | 3000.1502 | 2476.4225 | 1647.0023
Ger | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 85.8779 | 301.2488 | 346.8357 | 240.0923
Ita | 953.2113 | 968.1315 | 1066.3474 | 1205.9155 | 1106.7418 | 1371.9812 | 1410.7887 | 739.9061 | 1117.9155 | 1229.7277 | 1283.3052 | 1385.8685 | 1183.5305 | 1263.1455 | 1400.2637
Net | 1079.1174 | 987.1643 | 1238.5915 | 1259.662 | 1212.0657 | 1314.4413 | 1427.6808 | 1447.5117 | 1636.0563 | 1815.1831 | 1603.8216 | 1503.5023 | 1473.6056 | 1404.2347 | 2002.6049
Spa | 2708.7606 | 2191.3427 | 2338.939 | 2212.0188 | 2317.5399 | 2401.3897 | 2404.8075 | 1752.9014 | 1951.7746 | 1756.77 | 2249.8873 | 2121.4178 | 1984.2629 | 2102.6009 | 2259.9437
UK | 3290.697 | 2028.485 | 2245.563 | 3049.958 | 1989.928 | 1413.474 | 881.874 | 1130.602 | 1938.764 | 1911.825 | 2377.318 | 3361.967 | 2604 | 2632 | 2821
Cro+Gre+Lit+Pol+Por | 1375.4554 | 1302.0282 | 1659.4178 | 1454.77 | 1997.7277 | 2019.662 | 2024.4038 | 1855.1925 | 1577.0798 | 1669.7277 | 1951.9624 | 1832.8451 | 1896.9296 | 1661.0516 | 1909.7433
Europe | 13598.226 | 12756.6356 | 11526.0801 | 12352.3187 | 11118.8402 | 11754.14 | 12428.2228 | 14095.5954 | 15129.407
Europe2 | 13361.7111 | 10611.8653 | 12376.1076 | 13391.0284 | 12542.4538 | 11318.7886 | 12138.2402 | 10904.5551 | 11546.7358 | 12214.1536 | 13888.3509 | 14915.3379 | 13544.8169 | 12836.0845 | 13417.1471 | 13598.226 | 12756.6356 | 11526.0801 | 12352.3187 | 11118.8402 | 11754.14 | 12428.2228 | 14095.5954 | 15129.407
y-o-y growth regas capacity | 2341.6667 | 2341.6667 | 2758.3333 | 2758.3333 | 2758.3333 | 2454.3333 | 2866.6667 | 2850 | 3158.3333

## Slide 8
LNG SENDOUT COMPARISON
Chart: LNG sendout in bcm
| 44562 | 44593 | 44621 | 44652 | 44682 | 44713 | 44743 | 44774 | 44805 | 44835 | 44866 | 44896 | 44927 | 44958 | 44986 | 45017 | 45047 | 45078 | 45108 | 45139 | 45170 | 45200 | 45231 | 45261
Bel | 777.8727 | 642.9455 | 725.5455 | 1049.2364 | 780.3455 | 1025.3455 | 1129.9727 | 905.6545 | 753.9273 | 1036.0727 | 1095.9364 | 1094.3636 | 1066.0545 | 919.5727 | 1100.3356
Fra | 3050.7727 | 2392.0273 | 2979.9273 | 3025.5545 | 3013.4273 | 1683.4727 | 2731.8 | 2946.2 | 2465.4182 | 2672.9545 | 3185.4182 | 3382.3727 | 2904.6909 | 2397.6273 | 1594.5977
Ger | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 83.1455 | 291.6636 | 335.8 | 232.453
Ita | 922.8818 | 937.3273 | 1032.4182 | 1167.5455 | 1071.5273 | 1328.3273 | 1365.9 | 716.3636 | 1082.3455 | 1190.6 | 1242.4727 | 1341.7727 | 1145.8727 | 1222.9545 | 1355.7098
Net | 1044.7818 | 955.7545 | 1199.1818 | 1219.5818 | 1173.5 | 1272.6182 | 1382.2545 | 1401.4545 | 1584 | 1757.4273 | 1552.7909 | 1455.6636 | 1426.7182 | 1359.5545 | 1938.8856
Spa | 2622.5727 | 2121.6182 | 2264.5182 | 2141.6364 | 2243.8 | 2324.9818 | 2328.2909 | 1697.1273 | 1889.6727 | 1700.8727 | 2178.3 | 2053.9182 | 1921.1273 | 2035.7 | 2188.0364
UK | 3290.697 | 2028.485 | 2245.563 | 3049.958 | 1989.928 | 1413.474 | 881.874 | 1130.602 | 1938.764 | 1911.825 | 2377.318 | 3361.967 | 2604 | 2632 | 2821
Cro+Gre+Lit+Pol+Por | 1331.6909 | 1260.6 | 1606.6182 | 1408.4818 | 1934.1636 | 1955.4 | 1959.9909 | 1796.1636 | 1526.9 | 1616.6 | 1889.8545 | 1774.5273 | 1836.5727 | 1608.2 | 1848.9788
Europe | 13269.1944 | 12420.8735 | 11210.9104 | 11994.1649 | 10807.8475 | 11448.4276 | 12100.425 | 13729.3362 | 14761.8034
Europe2 | 13041.2697 | 10338.7577 | 12053.7721 | 13061.9944 | 12206.6916 | 11003.6195 | 11780.0831 | 10593.5656 | 11241.0276 | 11886.3523 | 13522.0907 | 14547.7306 | 13196.7 | 12511.4091 | 13079.997 | 13269.1944 | 12420.8735 | 11210.9104 | 11994.1649 | 10807.8475 | 11448.4276 | 12100.425 | 13729.3362 | 14761.8034
y-o-y growth regas capacity | 2341.6667 | 2341.6667 | 2758.3333 | 2758.3333 | 2758.3333 | 2454.3333 | 2866.6667 | 2850 | 3158.3333
Chart: LNG sendout in bcm
| 44562 | 44593 | 44621 | 44652 | 44682 | 44713 | 44743 | 44774 | 44805 | 44835 | 44866 | 44896 | 44927 | 44958 | 44986 | 45017 | 45047 | 45078 | 45108 | 45139 | 45170 | 45200 | 45231 | 45261
Bel | 777.8727 | 642.9455 | 725.5455 | 1049.2364 | 780.3455 | 1025.3455 | 1129.9727 | 905.6545 | 753.9273 | 1036.0727 | 1095.9364 | 1094.3636 | 1066.0545 | 919.5727 | 1188.7364 | 1254.6909 | 972.1475
Fra | 3050.7727 | 2392.0273 | 2979.9273 | 3025.5545 | 3013.4273 | 1683.4727 | 2731.8 | 2946.2 | 2465.4182 | 2672.9545 | 3185.4182 | 3382.3727 | 2904.6909 | 2397.6273 | 1248.9182 | 2318.9364 | 2865.068
Ger | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 83.1455 | 291.6636 | 335.8 | 325.0818 | 548.8364 | 624.9684
Ita | 922.8818 | 937.3273 | 1032.4182 | 1167.5455 | 1071.5273 | 1328.3273 | 1365.9 | 716.3636 | 1082.3455 | 1190.6 | 1242.4727 | 1341.7727 | 1145.8727 | 1222.9545 | 1419.4818 | 1327.4818 | 1148.3778
Net | 1044.7818 | 955.7545 | 1199.1818 | 1219.5818 | 1173.5 | 1272.6182 | 1382.2545 | 1401.4545 | 1584 | 1757.4273 | 1552.7909 | 1455.6636 | 1426.7182 | 1359.5545 | 1942.0364 | 1896.1273 | 1945.7771
Spa | 2622.5727 | 2121.6182 | 2264.5182 | 2141.6364 | 2243.8 | 2324.9818 | 2328.2909 | 1697.1273 | 1889.6727 | 1700.8727 | 2178.3 | 2053.9182 | 1921.1273 | 2035.7 | 2188.0364 | 2307.3727 | 2049.8306
UK | 3290.697 | 2028.485 | 2245.563 | 3049.958 | 1989.928 | 1413.474 | 881.874 | 1130.602 | 1938.764 | 1911.825 | 2377.318 | 3361.967 | 2604 | 2632 | 2945 | 2760 | 2542
Cro+Gre+Lit+Pol+Por | 1331.6909 | 1260.6 | 1606.6182 | 1408.4818 | 1934.1636 | 1955.4 | 1959.9909 | 1796.1636 | 1526.9 | 1616.6 | 1889.8545 | 1774.5273 | 1833.6273 | 1521.7182 | 1519.4364 | 1513.5455 | 1787.2387
Europe | 11210.9104 | 11994.1649 | 10807.8475 | 11448.4276 | 12100.425 | 13729.3362 | 14761.8034
Europe2 | 13041.2697 | 10338.7577 | 12053.7721 | 13061.9944 | 12206.6916 | 11003.6195 | 11780.0831 | 10593.5656 | 11241.0276 | 11886.3523 | 13522.0907 | 14547.7306 | 13193.7545 | 12424.9273 | 12776.7273 | 13926.9909 | 13935.4081 | 11210.9104 | 11994.1649 | 10807.8475 | 11448.4276 | 12100.425 | 13729.3362 | 14761.8034
y-o-y growth regas capacity | 2758.3333 | 2758.3333 | 2758.3333 | 2454.3333 | 2866.6667 | 2850 | 3158.3333

## Slide 9
2022 max: 96% (13 Nov)
Price as a major factor impacting demand and thus S+D balance in 2023
Bottom limit ~ 85-90% - regulatory channel
Top limit ~ 95% - price channel
Discussion
Industrial demand destruction
China recovery
World economy
Gas to power (nuclear + renewables load factor etc.)
Fuel switching
Russian flows
Storage
+31 bcm
Impact of storage level on 1 Apr y-o-y
-23 bcm
Impact of lower RU flows for 4-12/2023
Chart: Supply/demand balance in mcm/d + storage fill in % (base case)
| 44986 | 45017 | 45047 | 45078 | 45108 | 45139 | 45170 | 45200 | 45231 | 45261
Flows | 703.6226 | 760.727 | 790.28 | 733.6504 | 701.8704 | 600.2495 | 562.1841 | 552.1056 | 487.3001 | 512.4613 | 493.3653 | 540.4031 | 476.1265 | 494.4542 | 496.3192 | 480.8408 | 420.4612 | 440.691 | 513.7893 | 462.7784 | 475.8614 | 516.4431 | 502.5617 | 551.7033
Production | 257.6261 | 239.0684 | 234.2352 | 248.4194 | 226.8346 | 210.5399 | 215.0869 | 204.3269 | 235.377 | 216.6365 | 231.603 | 238.0688 | 238.4616 | 223.2627 | 218.817 | 231.0798 | 212.855 | 198.592 | 202.2394 | 191.6504 | 220.2134 | 205.0584 | 217.216 | 223.1942
Demand | -1939.8382 | -1710.8924 | -1534.9963 | -1188.7999 | -853.0637 | -798.7407 | -789.4593 | -720.2524 | -832.8509 | -907.7764 | -1267.7971 | -1611.9074 | -1830.1831 | -1706.4284 | -1429.9164 | -1085.3152 | -874.9508 | -771.4614 | -782.2221 | -739.2669 | -855.1473 | -1082.457 | -1491.9818 | -1638.8288
LNG | 431.0223 | 378.9945 | 399.2299 | 446.3651 | 404.5953 | 377.2936 | 391.5528 | 351.7632 | 384.8956 | 394.0013 | 462.9441 | 481.1363 | 436.9293 | 458.4279 | 424.2025 | 453.2742 | 411.5044 | 384.2027 | 398.4619 | 358.6723 | 391.8047 | 400.9104 | 469.8532 | 488.0454
Fullness % | 0.37957 | 0.29541 | 0.26809 | 0.33892 | 0.47764 | 0.58522 | 0.69589 | 0.80609 | 0.88704 | 0.9484 | 0.92883 | 0.83257 | 0.72049 | 0.60938 | 0.55695 | 0.57946 | 0.62732 | 0.69834 | 0.79197 | 0.86913 | 0.93471 | 0.94597 | 0.86077 | 0.75485
net inj | -182.5084 | 79.8796 | 169.8699 | 252.0243 | 332.2684 | 273.8342 | 232.7323 | 39.9548 | -302.3509 | -375.8859

## Slide 10
Chart: Supply/demand balance in mcm/d + storage fill in % (base case)
| 44986 | 45017 | 45047 | 45078 | 45108 | 45139 | 45170 | 45200 | 45231 | 45261
Flows | 703.6226 | 760.727 | 790.28 | 733.6504 | 701.8704 | 600.2495 | 562.1841 | 552.1056 | 487.3001 | 512.4613 | 493.3653 | 540.4031 | 476.1265 | 494.4542 | 496.3192 | 480.8408 | 420.4612 | 440.691 | 513.7893 | 462.7784 | 475.8614 | 516.4431 | 502.5617 | 551.7033
Production | 257.6261 | 239.0684 | 234.2352 | 248.4194 | 226.8346 | 210.5399 | 215.0869 | 204.3269 | 235.377 | 216.6365 | 231.603 | 238.0688 | 238.4616 | 223.2627 | 218.817 | 231.0798 | 212.855 | 198.592 | 202.2394 | 191.6504 | 220.2134 | 205.0584 | 217.216 | 223.1942
Demand | -1939.8382 | -1710.8924 | -1534.9963 | -1188.7999 | -853.0637 | -798.7407 | -789.4593 | -720.2524 | -832.8509 | -907.7764 | -1267.7971 | -1611.9074 | -1830.1831 | -1706.4284 | -1429.9164 | -1085.3152 | -874.9508 | -771.4614 | -782.2221 | -739.2669 | -855.1473 | -1082.457 | -1491.9818 | -1638.8288
LNG | 431.0223 | 378.9945 | 399.2299 | 446.3651 | 404.5953 | 377.2936 | 391.5528 | 351.7632 | 384.8956 | 394.0013 | 462.9441 | 481.1363 | 436.9293 | 458.4279 | 424.2025 | 453.2742 | 411.5044 | 384.2027 | 398.4619 | 358.6723 | 391.8047 | 400.9104 | 469.8532 | 488.0454
Fullness % | 0.37957 | 0.29541 | 0.26809 | 0.33892 | 0.47764 | 0.58522 | 0.69589 | 0.80609 | 0.88704 | 0.9484 | 0.92883 | 0.83257 | 0.72049 | 0.60938 | 0.55695 | 0.57946 | 0.62732 | 0.69834 | 0.79197 | 0.86913 | 0.93471 | 0.94597 | 0.86077 | 0.75485
net inj | -182.5084 | 79.8796 | 169.8699 | 252.0243 | 332.2684 | 273.8342 | 232.7323 | 39.9548 | -302.3509 | -375.8859
Chart: Supply/demand balance in mcm/d + storage fill in % (base case)
| 44986 | 45017 | 45047 | 45078 | 45108 | 45139 | 45170 | 45200 | 45231 | 45261
Flows | 710.0381 | 767.2071 | 796.7679 | 740.3104 | 708.4265 | 606.7175 | 568.5758 | 558.6158 | 493.7582 | 519.0571 | 499.6506 | 546.9261 | 477.1991 | 496.6971 | 507.5583 | 517.7473 | 441.9715 | 447.9042 | 520.9261 | 470.0339 | 483.0647 | 523.784 | 509.5921 | 558.9715
Production | 268.585 | 250.0273 | 245.1941 | 259.3783 | 237.7935 | 221.4988 | 226.0458 | 215.2858 | 246.3359 | 227.5954 | 242.5619 | 249.0277 | 249.4205 | 234.2216 | 229.7759 | 242.0387 | 223.8139 | 209.5509 | 213.1983 | 202.6093 | 231.1723 | 216.0173 | 228.1749 | 234.1531
Demand | -1939.8382 | -1710.8924 | -1534.9963 | -1188.7999 | -853.0637 | -798.7407 | -789.4593 | -720.2524 | -832.8509 | -907.7764 | -1267.7971 | -1611.9074 | -1830.1831 | -1706.4284 | -1429.9164 | -1085.3152 | -874.9508 | -771.4614 | -782.2221 | -739.2669 | -855.1473 | -1082.457 | -1491.9818 | -1638.8288
LNG | 420.6855 | 369.2407 | 388.8319 | 435.3974 | 393.7642 | 366.7879 | 379.9995 | 341.7311 | 374.7052 | 383.4272 | 450.7354 | 469.2781 | 425.6047 | 443.7448 | 412.0035 | 464.2336 | 449.529 | 373.697 | 386.9085 | 348.6402 | 381.6143 | 390.3363 | 457.6445 | 476.1872
Fullness % | 0.37954 | 0.29533 | 0.26795 | 0.33873 | 0.47745 | 0.5851 | 0.69586 | 0.80612 | 0.88714 | 0.94847 | 0.92885 | 0.83252 | 0.72044 | 0.6093 | 0.55746 | 0.59571 | 0.66536 | 0.74061 | 0.83879 | 0.92051 | 0.99026 | 1.0041 | 0.91814 | 0.81106
net inj | 240.3636 | 259.6908 | 338.8108 | 282.0165 | 240.704 | 47.6806 | -296.5703 | -369.517

## Slide 11
SENSItivity scenarios (demand and lng)
Chart: 15% demand reduction
| 45078 | 45108 | 45139 | 45170 | 45200 | 45231
High case LNG | 0.75624 | 0.86719 | 0.961 | 1.045 | 1.0783 | 1.0214
Base case LNG | 0.74087 | 0.8467 | 0.93539 | 1.0143 | 1.0424 | 0.98042
Low case LNG | 0.7255 | 0.8262 | 0.90977 | 0.98354 | 1.0065 | 0.93943
Chart: 10% demand reduction
| 45078 | 45108 | 45139 | 45170 | 45200 | 45231
High case LNG | 0.71371 | 0.81246 | 0.89475 | 0.96545 | 0.98184 | 0.90176
Base case LNG | 0.69834 | 0.79197 | 0.86913 | 0.93471 | 0.94597 | 0.86077
Low case LNG | 0.68297 | 0.77148 | 0.84352 | 0.90397 | 0.91011 | 0.81979
Chart: 5% demand reduction
| 45078 | 45108 | 45139 | 45170 | 45200 | 45231
High case LNG | 0.67118 | 0.75774 | 0.8285 | 0.88589 | 0.88541 | 0.78211
Base case LNG | 0.65581 | 0.73724 | 0.80288 | 0.85515 | 0.84954 | 0.74113
Low case LNG | 0.64044 | 0.71675 | 0.77726 | 0.82441 | 0.81368 | 0.70014
Storages on a similar path as in 2022
  Strong demand reduction remains despite recent price moderation
  China recovery might do without ramping up LNG imports

## Slide 12
SENSItivity scenarios (demand and lng)
Chart: 15% demand reduction
| 45078 | 45108 | 45139 | 45170 | 45200 | 45231
High case LNG | 0.75624 | 0.86719 | 0.961 | 1.045 | 1.0783 | 1.0214
Base case LNG | 0.74087 | 0.8467 | 0.93539 | 1.0143 | 1.0424 | 0.98042
Low case LNG | 0.7255 | 0.8262 | 0.90977 | 0.98354 | 1.0065 | 0.93943
Chart: 10% demand reduction
| 45078 | 45108 | 45139 | 45170 | 45200 | 45231
High case LNG | 0.71371 | 0.81246 | 0.89475 | 0.96545 | 0.98184 | 0.90176
Base case LNG | 0.69834 | 0.79197 | 0.86913 | 0.93471 | 0.94597 | 0.86077
Low case LNG | 0.68297 | 0.77148 | 0.84352 | 0.90397 | 0.91011 | 0.81979
Chart: 5% demand reduction
| 45078 | 45108 | 45139 | 45170 | 45200 | 45231
High case LNG | 0.67118 | 0.75774 | 0.8285 | 0.88589 | 0.88541 | 0.78211
Base case LNG | 0.65581 | 0.73724 | 0.80288 | 0.85515 | 0.84954 | 0.74113
Low case LNG | 0.64044 | 0.71675 | 0.77726 | 0.82441 | 0.81368 | 0.70014
Chart: 15% demand reduction
| 45078 | 45108 | 45139 | 45170 | 45200 | 45231
High case LNG | 0.77227 | 0.88827 | 0.98711 | 1.0758 | 1.1122 | 1.0555
Base case LNG | 0.76701 | 0.87773 | 0.9713 | 1.0547 | 1.0859 | 1.0238
Low case LNG | 0.76174 | 0.86719 | 0.9555 | 1.0337 | 1.0596 | 0.99223
Chart: 10% demand reduction
| 45078 | 45108 | 45139 | 45170 | 45200 | 45231
High case LNG | 0.74588 | 0.84933 | 0.93632 | 1.0113 | 1.0304 | 0.94975
Base case LNG | 0.74061 | 0.83879 | 0.92051 | 0.99026 | 1.0041 | 0.91814
Low case LNG | 0.73534 | 0.82826 | 0.90471 | 0.96919 | 0.97774 | 0.88653
Chart: 5% demand reduction
| 45078 | 45108 | 45139 | 45170 | 45200 | 45231
High case LNG | 0.71949 | 0.81039 | 0.88553 | 0.94686 | 0.9486 | 0.84406
Base case LNG | 0.71422 | 0.79986 | 0.86972 | 0.92579 | 0.92226 | 0.81245
Low case LNG | 0.70895 | 0.78932 | 0.85392 | 0.90471 | 0.89592 | 0.78083