## Slide 2: Insights on H2 velocity in wells
IGU Storage Committee Meeting 10 - 12 April 2024
Mejda AZABOU, Ph.D., Salt Cavern Engineer, Storengy

## Slide 3: Scope of the study
  Focus on salt caverns wells, simple regular linear tubing:
  30 bar < P < 250 bar ; 10°C < T < 50°C
  Study based on a literature review + operation history of Storengy gas storage sites

## Slide 4: Natural gas: current practice, state of the art
  What’s the current maximum velocity for natural gas ?
   15 m/s, 20 m/s, 14 m/s and 12 m/s
  How was this limit established ?
  Not known precisely, but the main aspects taken into accounts are:
    Erosion risk
    External noise
    Flow induced vibrations
    Flow induced pulsations
    Technical-economical aspects

## Slide 5: In order to establish H2 maximum velocity
  Erosion
  API RP 14E (identical to ISO-137032003-03)
  Pick-up velocity
  DNV-RP-O501
  Flow induced vibrations
  Wall pressure fluctuations (Von Karman Institute for fluid dynamics)
    Energy Institute Guidelines (EIG)
  Flow induced pulsations
  Energy Institute Guidelines (EIG)
  External Noise

## Slide 6: Erosion: API RP 14E / ISO-137032003-03
ρ * V2 = C
Empirical equation, no solid particles, no corrosive agents ( H2S or CO2)
The erosional velocity depends on the gas density which, in turn, depends on the pressure.
Defining one maximum velocity over a large range of pressure is extremely conservative.
Need to define a maximum velocity by pressure ranges.
The API RP 14E = ISO-137032003-03, widely utilized but also criticized : unknown origin, limitations, inadequacy to predict erosion…

## Slide 7
Erosion: Pick-up velocity
  The pick-up velocity of a gas flowing inside a pipe of diameter , is the minimum speed sufficient to move a layer of solid particles of mean diameter and density , initially at rest.
  (Empirical model of Cabrejos & Klinzing, Von Karman Institute of Fluid Dynamics)
 Depending on the pressure, H2 can flow 4.6 to 6.5 times faster than natural gas without increasing the risk of erosion.

## Slide 8
Erosion: DNV-RP-O501
  Directives on “how to operate safely and cost effectively manage the consequences of sand produced from the oil and gas reservoirs through production wells, flowlines and processing facilities” & “Erosive wear in piping systems”
  If no solid particles: 70 to 80 m/s
  In presence of solid particles, for linear pipes:
  
If V(H2) is 3 to 4 times greater than V(GN), erosion risk will increase 20 to 40 times.
X Too conservative and non consistent with Pick-up velocity and API RP 14E.

## Slide 9: Flow induced vibrations : wall pressure fluctuations
Turbulent flow boundary  wall pressure fluctuation  vibrations
(empirical model, Goody model: Von Karman Institute of Fluid Dynamics)
Reynolds number () is the main driving parameter
(DNV Energy Systems. GERG Energy Capacity Study. Energy capacity related effects of repurposing
natural gas pipelines for hydrogen or hydrogen blends. Flow and Fuel Advisory.
Groningen : DNV Energy Systems, 2022. 228024-FFA 22-1838 Rev.2)
 low/no risk of vibration if H2 velocity is 3 to 4 times greater than NG
Pressure (bar) | V(H2)/V(NG) | Re(H2)/Re(GN)
4 | 3,081 | 0,465
8 | 3,114 | 0,465
16 | 3,183 | 0,467
30 | 3,309 | 0,469
40 | 3,403 | 0,475
60 | 3,596 | 0,496
85 | 3,842 | 0,520
120 | 4,149 | 0,557
150 | 4,326 | 0,697
250 | 4,279 | 0,943

## Slide 10: Conclusions and recommended maximum velocity
Establish maximum velocities by pressure ranges rather than a potentially extremely conservative unique value.
Recommended H2 velocities in wells, based on the most conservative erosion assessment method:
Elements on the maximum H2 velocity in wells  complete with a study focused on surface facilities + thermomechanical study.
Most norms were initially established for oil & gas industry.
Pressure | Maximum velocity H2 (m/s) | PC(H2)/PC(NG) (if V(NG)=15 m/s)
30 to 100 bar | 42 | 0,68 to 0,85
100 to 150 bar | 35 | 0,52 to 0,57
150 to 200 bar | 30 | 0,44 to 0,52
200 to 250 bar | 28 | 0,41 to 0,43
Pressure | Maximum velocity H2 (m/s)
30 to 100 bar | 42
100 to 150 bar | 35
150 to 200 bar | 30
200 to 250 bar | 28

## Slide 11: Thank you !