## Slide 1: Noise emission reduction project in UGS Kosakowo
Sławomir Skwarczyński
Paris, April 2024

## Slide 2
About the project
The main aim of the project was to reduce noise emission by the installation of UGS Kosakowo, especially for low frequency emission.
Implementation of the designed solutions resulted in significant environmental impact and improvement of acoustic comfort for neighbouring residents within the range of UGS influence.
Noise emission issues
the social party
local authorities
Legal reqirements

## Slide 3: Why we did it
Allowed noise levels:
Type of area | Day | Night
Residential area (single-family housing) | 50 dBA | 40 dBA
Residential area (multi-family housing) | 55 dBA | 45 dBA

## Slide 4
Project overview
Vibrodiagnostic analysys
Identification of the problem
2019/20
I Stage
Limiting of noise in main emitters
Accredited measurements
Acoustic camera measurements
Analysis of the results
2021/22
II Stage
Limiting of noise in secondary emitters, including low frequency sources
Accredited measurements
Analysis of the results
2023/24
Step-by-step approach to get best results with limited resources

## Slide 5
I Stage
– implemented solutions:
Silencers of ventilation air intake – 20 pcs.
Silencers of air supply fans intake – 12 pcs.
Entrance doors to compressor building – 8 pcs.
Insulation of technological installation – 8 pcs.
Silencers of air intake to gas engine’s turbines – 8 pcs.

## Slide 6
Intake of ventilation air
Gravity ventilation intake 73dB/A 68dB/A reduction: 5dB/A
Fan intake 84dB/A 68dB/A reduction: 16dB/A

## Slide 7
Entrance door
79dB/A 63dB/A reduction: 16dB/A

## Slide 8
Scrubber installation with piping
80 dB/A 67 dB/A reduction: 13 dB/A

## Slide 9
Silencers of air intake to gas engine’s turbines
96 dB/A 73 dB/A reduction: 23 dB/A

## Slide 10
Silencers of air intake to gas engine’s turbines

## Slide 11
Accredited noise measurements after I stage

## Slide 12
Acoustic camera measurements after I Stage
Mode of acoustic emission at low frequency
Mode in bandwidth 63 and 125Hz
(stack)

## Slide 13
I Stage – summary
Required efficiency of all implemented noise reduction measures have been achieved
Significant reduction of noise level on-site and in the UGS surrounding
Analysis of the accredited measurements allowed to show low frequency noise issue
Additional emitters to work on during II Stage have been selected – exhaust stacks of gas engines 4 psc.

## Slide 14
II Stage:
Main Focus on low frequency noise emission reduction from other emiters.
Exhaust stacks – two directions of noise emission through the outlet and blow-off flap.

## Slide 15
Goals
To reach adequate acoustic conditions it was required to cut the noise emission from exhaust stacks by at least 14,0 dB/A.
Main focus were 63 and 125 Hz bands, which are responsible for low frequency noise transmission
Octave band center frequencies [Hz]
Acoustic pressure level L [dB/A]

## Slide 16
Silencers on the gas engine exhaust gases stack outlet – 4 psc.
Noise reduction level 18,6 dB/A 95,5 → 76,8 dB/A
Silencers on blow-off flaps – 4 pcs.
Noise reduction level 15,4 dB/A 82,1 → 66,7 dB/A
Exchange of acoustic insulation of stack – 4 pcs.
Noise reduction level 15,8 dB/A 79,4 → 63,6 dB/A
II stage – implemented solutions
Silencer on the outlet
Insulation of stack
Silencer on the blow-off flap

## Slide 17
Accredited noise level measurements after II Stage
Based on the performed measurements and calculations it has been confirmed that on all measurement points around UGS Kosakowo both, during the day and night while running 3 compressor units at full capacity, noise level was within allowed limits.
Measurement results | 
Day | Night
33-42 dB/A | 32-33 dB/A
Background noise level | 
N/A (due to traffic noise) | 31,6 dB/A

## Slide 18
II Stage – summary
Noise reduction level was higher than expected for all emitters
Low frequency noise at residential areas in Kosakowo were significantly reduced
Accredited measurements results and analysis based on those results confirmed that the impact of UGS Kosakowo installations on acoustic environment of residential areas is within allowed limits
II Stage implementation period - 12 months

## Slide 19: Q&A