## Slide 1: Model 2030-2040
Monthly flexibility need analysis

## Slide 2
EU Gas consumption to decrease, flexibility questionable
Key trends:
  Electrification (HPs, EVs, industry)
  More intermittent generation
  Insulation and other efficiency measures
  Decarbonization
Chart: Production & consumption of electricity in 2022
| Consumption | Production
Other demand | 2629.2327
EV demand | 13.56
HP demand | 134.2373
Wind | 419.95
Solar | 210.75
Nuclear | 609.26
Gas | 534.72
Coal | 448.77
Hydro | 276.24
Oil/Other fossil | 105.38
Others | 171.96
Power supply, of which: | 2777.03 | 2777.03
Chart: Production & consumption of electricity in 2040
| Consumption | Production
Other demand | 2476.1162
EV demand | 389.172
HP demand | 402.7118
Wind | 1100
Solar | 484
Nuclear | 689
Gas | 256.0246
Coal | 74.2383
Hydro | 333.7371
Oil/Other fossil | 7
Others | 324
Power supply, of which: | 3268 | 3268
Chart: Gas to power + Heating demand
| 2022* | 2030 | 2040
Heating | 1388.7894 | 1188.1209 | 1038.2199
Gas to power | 1114 | 864.7991 | 449.166
Sum | 2502.7894 | 2052.92 | 1487.3858
Assumed efficiency of gas power plants | 0 | 0 | 0

## Slide 3
Power demand to increase, to be matched with renewables
The charts present two different scenarios
  Equinor (Walls) - current trends, economic growth remains the key driver, energy transition that is slowly accelerating, but does not reach climate targets
  Ember (Stated policies) - pathway aligned with stated national policies until 2035 (afterwards trajectory of zero emissions in the power sector at least cost by 2050 due to a lack of detail in official plans)
We consider Walls scenario more likely and we will use it to demonstrate our approach, however in the sensitivity analysis we will discuss various options
In Walls scenario Power demand to grow by 10% by 2030 (+266 TWh) and 18% by 2040 (+491 TWh)
  Decline in fossil sources (-675 TWh by 2040) to be offset by
  Growth in intermittent sources (+953 TWh by 2040) – what about their seasonal profile?
Chart: Power supply by source: 2022 / 2030 / 2040
| 2022 | 2030 | 2040 | Ember | Equinor-Walls | Equinor-Walls
Wind | 419.95 | 730 | 1100
Solar | 210.75 | 310 | 484
Nuclear | 609.26 | 689 | 689
Gas | 534.72 | 396 | 244
Coal | 448.77 | 298 | 83
Hydro | 276.24 | 334 | 337
Oil | 105.38 | 33 | 7
Others | 171.96 | 253 | 324
Power supply, of which: | 2777.03 | 3043 | 3268
Chart: Power supply by source: 2022 / 2030 / 2040
| 2022 | 2030 | 2040 | Ember | Ember-Stated policies | Ember-Stated policies
Wind | 419.95 | 957.217 | 2029.4834
Solar | 210.75 | 449.7796 | 1095.8785
Nuclear | 609.26 | 618.62 | 322.3252
Gas | 534.72 | 450.3121 | 438.82
Coal | 448.77 | 41.5425 | 4.4448
Hydro | 276.24 | 334.7429 | 334.6082
Oil | 105.38 | 0.29246 | 0.55342
Others | 171.96 | 147.0419 | 132.3897
Power supply, of which: | 2777.03 | 2999.5487 | 4358.5033

## Slide 4
Supply: seasonal Swing being provided by gas, nuclear & coal
Current annual power consumption (& power supply): 2,777 TWh (2022)
We have applied 2017-2022 monthly profile on annual net electricity generation in 2022 as shown in the chart
Wind & solar can supplement each other smoothening the monthly pattern (using ratio 2.3:1 due to load factors of 24% & 11% respectively
Others of 172 TWh include bioenergy, geothermal, ocean, etc.
Seasonal swing (Oct-Mar vs Apr-Sep) of 189 TWh delivered mostly by gas (60 TWh), nuclear (48 TWh) and coal (47 TWh)
In the future seasonality will change (mainly due to heat pumps and electric vehicles)
Chart: Power supply seasonality (based on 2017-2022 monthly profiles)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Wind | 43.7091 | 43.8501 | 39.6541 | 32.3023 | 27.8946 | 23.2192 | 23.6106 | 24.6146 | 29.0144 | 43.5595 | 40.4368 | 48.0847
Solar | 6.4823 | 10.1381 | 17.1321 | 22.2684 | 25.7585 | 27.3699 | 28.0007 | 25.6702 | 20.122 | 14.3855 | 7.7229 | 5.6996
Nuclear | 62.0162 | 54.4377 | 55.6473 | 48.9 | 46.1921 | 44.7413 | 47.1882 | 47.1589 | 46.5125 | 49.087 | 50.5536 | 56.8252
Gas | 55.9869 | 46.636 | 45.1382 | 35.9301 | 35.0333 | 38.9506 | 44.3169 | 41.8537 | 41.4356 | 44.774 | 53.0986 | 51.5661
Coal | 46.6965 | 39.2125 | 39.108 | 32.2542 | 30.9569 | 31.3597 | 34.3086 | 35.1854 | 36.9943 | 38.3051 | 42.5897 | 41.7991
Hydro | 25.0375 | 23.2834 | 25.254 | 23.6538 | 26.6406 | 25.0683 | 22.3583 | 20.4701 | 18.6936 | 18.8125 | 21.7256 | 25.2421
Oil/Other fossil | 9.7118 | 8.3053 | 8.5266 | 7.6929 | 8.1717 | 8.5734 | 9.4931 | 9.7434 | 9.1718 | 8.8216 | 8.3748 | 8.7936
Others | 20.203 | 16.5294 | 18.5039 | 14.3595 | 14.0933 | 11.8414 | 12.8964 | 11.0215 | 11.1538 | 9.9413 | 14.5859 | 16.8306

## Slide 5
DEMAND: HP penetration to affect Seasonal pattern
Electric vehicles (EVs) assumptions
Current penetration and consumption (2022): 6 mil. EVs (14 TWh)
2030/2040: 35/140 mil. EVs
Annual mileage: 11,300 km/car (2022) +23% in 2030/2040)
Avg. consumption: 0.2 kWh/km
Rather complex seasonality as mileage peaks in Sum while battery drain in Win
Heat pumps (HPs) assumptions
Consumption in 2022: 134 TWh
Number of units 2022: 20 mil. HPs of which 90% is used for space heating
Number of units 2030 / 2040: 40 mil. (Fit for 55) / 60 mil. (own assumption)
Highly seasonal consumption
To be further discussed in detail
Other power demand
By 2040 EVs to grow by 1770% (375 TWh), HPs by 200% (268 TWh), the remainder drops by 6% (153 TWh) to be consistent with Equinor Walls
We have applied 2022 monthly profile on this remainder demand
Overall seasonal pattern will be more pronounced in 2030+, mainly due to HP
Chart: Power demand split (2022)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Power demand less EV & HP | 240.4523 | 221.0006 | 229.6816 | 205.2682 | 208.5808 | 209.9169 | 220.7336 | 214.2628 | 209.8637 | 219.2398 | 221.1547 | 229.0777
EV demand | 1.1122 | 1.0975 | 0.94759 | 0.89425 | 1.007 | 1.2068 | 1.4392 | 1.4551 | 1.1314 | 1.1228 | 0.93564 | 1.2106
HP demand | 28.2788 | 20.2944 | 18.335 | 11.1987 | 5.1531 | 0 | 0 | 0 | 2.1029 | 7.324 | 16.9976 | 24.5528
Chart: Power demand split (2040)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Power demand less EV & HP | 226.4493 | 208.1304 | 216.3058 | 193.3142 | 196.4338 | 197.6922 | 207.8789 | 201.785 | 197.6421 | 206.4721 | 208.2754 | 215.7371
EV demand | 31.9203 | 31.4984 | 27.1958 | 25.665 | 28.9006 | 34.635 | 41.3037 | 41.7603 | 32.4725 | 32.2235 | 26.8528 | 34.7441
HP demand | 84.8363 | 60.8831 | 55.005 | 33.5962 | 15.4594 | 0 | 0 | 0 | 6.3087 | 21.9719 | 50.9929 | 73.6584

## Slide 6
In 2030/40 more power balancing will be needed
Seasonal demand swing will increase due to rising share of heat pumps:
  189 TWh (6.8 % of annual) in 2022
  283 TWh (9.3 %) in 2030
  358 TWh (11 %) in 2040
All the sources apart from coal and gas are shown with the same seasonal pattern as in 2022 respecting the forecasted growth of each individual source
Coal+gas are used for balancing in our model. Their total share will decline notably from 35% in 2022 (983 TWh) to 10% in 2040 (330 TWh).
Seasonal pattern for coal+gas will be much more prominent
Chart: Power supply seasonality, 2040
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Winter | Summer | Winter
Wind | 114.4898 | 114.8593 | 103.8683 | 84.6113 | 73.0661 | 60.8194 | 61.8445 | 64.4746 | 75.9992 | 114.0979 | 105.9184 | 125.9512
Solar | 14.8869 | 23.2827 | 39.3448 | 51.1408 | 59.1558 | 62.8566 | 64.3053 | 58.9532 | 46.2113 | 33.0371 | 17.736 | 13.0896
Nuclear | 70.1329 | 61.5625 | 62.9305 | 55.3 | 52.2377 | 50.597 | 53.3642 | 53.3311 | 52.6001 | 55.5116 | 57.1701 | 64.2625
Hydro | 30.5446 | 28.4047 | 30.8087 | 28.8566 | 29.2375 | 30.5822 | 27.2761 | 24.9726 | 22.8053 | 22.9504 | 26.5042 | 30.7942
Oil/Other fossil | 0.64512 | 0.55169 | 0.56639 | 0.51101 | 0.54282 | 0.5695 | 0.63059 | 0.64722 | 0.60925 | 0.58599 | 0.55631 | 0.58412
Others | 38.0657 | 31.144 | 34.8642 | 27.0556 | 26.554 | 22.311 | 24.2989 | 20.7662 | 21.0155 | 18.731 | 27.4822 | 31.7115
Coal+gas | 74.4408 | 40.707 | 26.1237 | 5.1001 | 0 | 4.5915 | 17.463 | 20.4004 | 17.1825 | 15.7536 | 50.7538 | 57.7465
Chart: Power supply seasonality, 2022
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Winter | Summer | Winter
Wind | 43.7091 | 43.8501 | 39.6541 | 32.3023 | 27.8946 | 23.2192 | 23.6106 | 24.6146 | 29.0144 | 43.5595 | 40.4368 | 48.0847
Solar | 6.4823 | 10.1381 | 17.1321 | 22.2684 | 25.7585 | 27.3699 | 28.0007 | 25.6702 | 20.122 | 14.3855 | 7.7229 | 5.6996
Nuclear | 62.0162 | 54.4377 | 55.6473 | 48.9 | 46.1921 | 44.7413 | 47.1882 | 47.1589 | 46.5125 | 49.087 | 50.5536 | 56.8252
Hydro | 25.0375 | 23.2834 | 25.254 | 23.6538 | 26.6406 | 25.0683 | 22.3583 | 20.4701 | 18.6936 | 18.8125 | 21.7256 | 25.2421
Oil/Other fossil | 9.7118 | 8.3053 | 8.5266 | 7.6929 | 8.1717 | 8.5734 | 9.4931 | 9.7434 | 9.1718 | 8.8216 | 8.3748 | 8.7936
Others | 20.203 | 16.5294 | 18.5039 | 14.3595 | 14.0933 | 11.8414 | 12.8964 | 11.0215 | 11.1538 | 9.9413 | 14.5859 | 16.8306
Coal+gas | 102.6834 | 85.8484 | 84.2462 | 68.1843 | 65.9901 | 70.3103 | 78.6255 | 77.0391 | 78.4299 | 83.0791 | 95.6883 | 93.3652
Chart: Coal plants phase-out
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
DE | 46.774 | 43.2215 | 39.669 | 38.795 | 29.257 | 28.745 | 28.451 | 28.451 | 25.681 | 22.769 | 15.257 | 15.257 | 8.436 | 7.456 | 7.456 | 7.456 | 7.456 | 0 | 0 | 0
PL | 28.016 | 28.357 | 28.698 | 27.966 | 27.207 | 27.207 | 27.207 | 27.207 | 26.733 | 26.733 | 26.733 | 26.733 | 26.733 | 26.733 | 26.733 | 21.703 | 21.703 | 21.703 | 21.703 | 21.703
Others | 51.464 | 47.5165 | 43.569 | 38.255 | 29.629 | 28.969 | 23.607 | 22.536 | 17.706 | 13.026 | 13.026 | 11.807 | 5.039 | 5.039 | 5.039 | 5.039 | 5.039 | 0 | 0 | 0

## Slide 7
Heating demand
We have split gas consumption into three segments:
  Gas to Power (89 bcm)
  Flat consumption (summer demand excluding GtP) which is mostly industrial demand (177 bcm)
  Remaining seasonal consumption - most of it being space heating (126 bcm)
Seasonal demand is well correlated with Heating Degree Days (HDDs)
  HDDs are calculated as Tm ≤ 15°C Then [HDD = ∑i(18°C - Tim)] Else [HDD = 0]
  We have used historical HDDs in calculating HP demand in connection with their varying efficiency
  HDDs as shown in the chart are based on daily data and weighted across 10 European countries by volume of consumption (also national data are weighted this way)
Chart: HDD distribution vs. Seasonal demand (2019-2022)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Seasonal demand (TWh) | 309.5262 | 222.9644 | 198.7905 | 99.2465 | 48.5203 | 0 | 0 | 0 | 13.6623 | 79.1417 | 169.4675 | 247.4698
HDD distribution (%) 2019-2022 | 0.19658 | 0.1468 | 0.13997 | 0.088929 | 0.042307 | 0.0025817 | 0.00024073 | 0.00081879 | 0.017437 | 0.059071 | 0.12868 | 0.17659
Chart: Gas consumption in TWh (2019-2022 avg.)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Flat consumption | 14.8854 | 14.8854 | 14.8854 | 14.8854 | 14.8854 | 14.8118 | 14.8854 | 13.5471 | 14.8854 | 14.8854 | 14.8854 | 14.8854
Seasonal consumption | 28.1387 | 20.2695 | 18.0719 | 9.0224 | 4.4109 | 0 | 0 | 0 | 1.242 | 7.1947 | 15.4061 | 22.4973
GtP | 9.5933 | 7.4444 | 7.4243 | 6.2539 | 5.6384 | 6.6062 | 7.7614 | 7.257 | 7.2599 | 7.3815 | 8.2756 | 8.4607

## Slide 8
Heat Pumps: Number of units to double by 2030
Existing stock (2022) of HPs used for space heating is 18 mil. (90% of 20 mil. shown in the chart)
This represents 13.7% share of heating market (in terms of number of buildings) and 5.1% share of power demand (134 TWh)
HP heating consumption of 134 TWh has been quantified as:
  Current residential consumption: 95 TWh (81 TWh sourced from Eurostat for 2021 + 17% increase in HP stock in 2022)
  We assume the same share of HPs on heating demand in non-residential sector
Average efficiency of HPs is modelled at 340% (ranging from 150% at -20 °C to 440% at 20 °C assuming heating medium temperature (Tw) of 43 °C as illustrated in the chart) resulting from our calculations with historical daily data
Seasonal profile utilizes HDDs. Due to varying efficiency the seasonality is slightly more pronounced than that of HDDs
HP heating consumption to increase in 2030 and 2040 to 268 and 403 TWh respectively, representing 8.8% and 12.3% share of the yearly power demand.
Heat Pump Efficiency Across Temperature
Source: REHVA Federation of European Heating, Ventilation and Air Conditioning Associations
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2030 | 2040
HP Stock | 10.5 | 11.74 | 13.21 | 14.77 | 16.87 | 20 | 22.3 | 40 | 60

## Slide 9
Building stock will be better insulated and with more HPs
Building stock: quality
Although there is 18 mil. HPs used for space heating in 2022, for this analysis (normalized buildings) we consider normalized figure of 23 mil. and also assume that HPs are used only in insulated buildings
We assume 20% (34 mil.) of normalized buildings are well insulated (and 23 mil. of them have HPs). The remaining 11 mil. will have HPs installed by 2040.
Increased share of well-insulated buildings will come either from replacement (1% p.a. mentioned above) and renovation (1% p.a. by 2030 & 1.5% p.a. in 2030-2040)
  RePowerEU target is 2.1% p.a. in 2030 (medium & deep renovation)
We estimate 32% energy saving resulting from insulating of a building (as an average of two sources mentioning 21% and 44%)
Chart: Normalized buildings: quality status
| 2022 | 2030 | 2040
Not insulated | 136000000 | 108800000 | 66300000
Insulated w/o HP (old) | 10791548.0545 | 5995304.4747
Insulated w/o HP (new) | 8787791.6343 | 34074644.1636
Insulated & HP | 23208451.9455 | 46416903.8909 | 69625355.8364
Total | 170000000 | 170000000 | 170000000
Chart: Number of buildings
Residential buildings | 119000000 | 120000000 | 120000000
Non residential buildings adjusted | 12000000 | 40000000 | 50000000
Total buildings adjusted | 131000000 | 160000000 | 170000000
Chart: Change in seasonal demand
| 2022 | 2030 | 2040
Seasonal demand | 1388.7894 | 1151.3233 | 865.813
Gas demand replaced | 237.4661 | 522.9764
Total | 1388.7894 | 1415.8396 | 1427.8541

## Slide 10
Seasonal profile to be more prominent
Annual gas consumption with seasonal element is assumed to decrease by 19.4% by 2030 and 47.5% by 2040
The decrease of seasonal swing will be much less dramatic: by 5.5% by 2030 and 16.9% by 2040
Decreasing need for seasonal swing in the heating segment will be partly offset by GtP segment
Chart: GtP + Heating demand
| 2022* | 2030 | 2040
Heating | 1388.7894 | 1151.3233 | 865.813
Gas to power | 1114 | 864.7991 | 449.166
Sum | 2502.7894 | 2016.1224 | 1314.979
Assumed efficiency of gas power plants | 0 | 0 | 0
Chart: GtP + Heating demand 2022
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 309.5262 | 222.9644 | 198.7905 | 99.2465 | 48.5203 | 0 | 0 | 0 | 13.6623 | 79.1417 | 169.4675 | 247.4698
Gas to power | 116.6394 | 97.1583 | 94.0379 | 74.8544 | 72.9859 | 81.1471 | 92.3268 | 87.1953 | 86.3242 | 93.2792 | 110.6221 | 107.4294
Chart: GtP + Heating demand 2030
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 256.601 | 184.8402 | 164.7997 | 82.2766 | 40.2239 | 0 | 0 | 0 | 11.3262 | 65.6095 | 140.4907 | 205.1555
Gas to power | 124.8556 | 85.1621 | 74.1833 | 46.3204 | 36.8728 | 45.8587 | 61.3189 | 60.8356 | 60.5168 | 62.8403 | 102.5743 | 103.4603
Chart: GtP + Heating demand 2040
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 192.9679 | 139.0027 | 123.932 | 61.8733 | 30.249 | 0 | 0 | 0 | 8.5175 | 49.3393 | 105.6512 | 154.2801
Gas to power | 115.6688 | 58.8793 | 33.3279 | 0 | 0 | 0 | 19.6682 | 24.5411 | 18.3174 | 15.3914 | 75.4256 | 87.9462

## Slide 11
Base case:
  20/40/60 mil. HPs
  2%/2.5% replacement + renovation
  6/35/140 mil. Evs
Higher share of solar on power supply results in higher swing (see the table)
Scenarios for power generation: Monthly profiles
S/W swing in TWh |  |  | 
Scenario | Eq - Walls | Ember - St. pol. | IEA - St. pol.
2022 | 1,190 |  | 
2030 | 1,125 | 1,166 | 1,243
Share of solar | 10% | 15% | 19%
Share of wind | 24% | 32% | 30%
2040 | 989 | 1,187 | 
Chart: GtP + Heating demand 2022
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 309.5262 | 222.9644 | 198.7905 | 99.2465 | 48.5203 | 0 | 0 | 0 | 13.6623 | 79.1417 | 169.4675 | 247.4698
Gas to power | 116.6394 | 97.1583 | 94.0379 | 74.8544 | 72.9859 | 81.1471 | 92.3268 | 87.1953 | 86.3242 | 93.2792 | 110.6221 | 107.4294
Chart: GtP + Heating demand 2030
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 256.601 | 184.8402 | 164.7997 | 82.2766 | 40.2239 | 0 | 0 | 0 | 11.3262 | 65.6095 | 140.4907 | 205.1555
Gas to power | 124.8556 | 85.1621 | 74.1833 | 46.3204 | 36.8728 | 45.8587 | 61.3189 | 60.8356 | 60.5168 | 62.8403 | 102.5743 | 103.4603
Chart: GtP + Heating demand 2040
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 192.9679 | 139.0027 | 123.932 | 61.8733 | 30.249 | 0 | 0 | 0 | 8.5175 | 49.3393 | 105.6512 | 154.2801
Gas to power | 115.6688 | 58.8793 | 33.3279 | 0 | 0 | 0 | 19.6682 | 24.5411 | 18.3174 | 15.3914 | 75.4256 | 87.9462
Chart: GtP + Heating demand 2030 (EMBER)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 256.601 | 184.8402 | 164.7997 | 82.2766 | 40.2239 | 0 | 0 | 0 | 11.3262 | 65.6095 | 140.4907 | 205.1555
Gas to power | 107.1902 | 56.6468 | 43.6072 | 10.8142 | 0.76093 | 9.7705 | 26.0167 | 25.5966 | 27.5537 | 20.861 | 77.5038 | 77.0711
Chart: GtP + Heating demand 2040 (EMBER)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 192.9679 | 139.0027 | 123.932 | 61.8733 | 30.249 | 0 | 0 | 0 | 8.5175 | 49.3393 | 105.6512 | 154.2801
Gas to power | 194.29 | 88.8167 | 55.4416 | 0 | 0 | 0 | 22.3744 | 26.8126 | 28.0516 | 5.0011 | 123.1149 | 133.1172
Chart: GtP + Heating demand 2030 (IEA)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 256.601 | 184.8402 | 164.7997 | 82.2766 | 40.2239 | 0 | 0 | 0 | 11.3262 | 65.6095 | 140.4907 | 205.1555
Gas to power | 103.2744 | 54.0784 | 31.0517 | 0 | 0 | 0 | 0 | 0.049358 | 7.4917 | 14.3323 | 79.9341 | 84.1094
The more rewewables installed – the greater need for flexibility from gas (storage)

## Slide 12: Thank you for your attention

## Slide 13
WE Focus on 2 segments of gas consumption: Heating & GtP
Scope: EU27
Annual gas consumption (2019-2022): 4,321 TWh ~ 393 bcm (using 11 kWh/m3) can be split into
  Gas to Power (GtP)
  Heating
  Other (non-seasonal, mainly industry)
Year 2023 shows signs of demand decrease of which a significant part wil be permanent – not reflected yet [TO DO]
Only GtP and Heating are volatile / seasonal, therefore we focus only on these
Chart: Avg. gas consumption in EU (2019-2022), Twh
| Non-seasonal | Gas to Power | Heating
 | 1964.8753 | 982.9215 | 1388.7894

## Slide 14
Coal/Gas switching: Coal diminishing, gas for flexibility
From calculated coal+gas power generation (top right chart) we assign volume to coal based on the pace of planned phase-out (as shown below) compared to current generation
Gas gets the remainder, which might be slightly conservative assumption (see Q2 in the bottom right chart)
Under certain scenarios coal+gas can turn negative - then hydro is curtailed first in our model
Chart: Coal+gas for power in 2040 (Walls scenario)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Coal+gas | 74.4408 | 40.707 | 26.1237 | 5.1001 | 0 | 4.5915 | 17.463 | 20.4004 | 17.1825 | 15.7536 | 50.7538 | 57.7465
Chart: Coal & gas split in 2040 (Walls scenario)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Gas | 65.9312 | 33.5612 | 18.9969 | 0 | 0 | 0 | 11.2109 | 13.9884 | 10.4409 | 8.7731 | 42.9926 | 50.1293
Coal | 8.5096 | 7.1458 | 7.1268 | 5.1001 | 0 | 4.5915 | 6.2522 | 6.4119 | 6.7416 | 6.9804 | 7.7612 | 7.6172
Chart: Coal plants phase-out
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
DE | 46.774 | 43.2215 | 39.669 | 38.795 | 29.257 | 28.745 | 28.451 | 28.451 | 25.681 | 22.769 | 15.257 | 15.257 | 8.436 | 7.456 | 7.456 | 7.456 | 7.456 | 0 | 0 | 0
PL | 28.016 | 28.357 | 28.698 | 27.966 | 27.207 | 27.207 | 27.207 | 27.207 | 26.733 | 26.733 | 26.733 | 26.733 | 26.733 | 26.733 | 26.733 | 21.703 | 21.703 | 21.703 | 21.703 | 21.703
Others | 51.464 | 47.5165 | 43.569 | 38.255 | 29.629 | 28.969 | 23.607 | 22.536 | 17.706 | 13.026 | 13.026 | 11.807 | 5.039 | 5.039 | 5.039 | 5.039 | 5.039 | 0 | 0 | 0

## Slide 15
HP sensitivity
HP in mil. units |  |  | 
Scenario | Slow | Base | Rapid
2022 |  | 20 | 
2030 | 34 | 40 | 50
2040 | 44 | 60 | 100
S/W swing in TWh |  |  | 
Scenario | Slow | Base | Rapid
2022 | 1,190 |  | 
2030 | 1,105 | 1,125 | 1,158
2040 | 922 | 989 | 1,114
Chart: GtP + Heating demand 2022
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 309.5262 | 222.9644 | 198.7905 | 99.2465 | 48.5203 | 0 | 0 | 0 | 13.6623 | 79.1417 | 169.4675 | 247.4698
Gas to power | 116.6394 | 97.1583 | 94.0379 | 74.8544 | 72.9859 | 81.1471 | 92.3268 | 87.1953 | 86.3242 | 93.2792 | 110.6221 | 107.4294
Chart: GtP + Heating demand 2030
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 256.601 | 184.8402 | 164.7997 | 82.2766 | 40.2239 | 0 | 0 | 0 | 11.3262 | 65.6095 | 140.4907 | 205.1555
Gas to power | 124.8556 | 85.1621 | 74.1833 | 46.3204 | 36.8728 | 45.8587 | 61.3189 | 60.8356 | 60.5168 | 62.8403 | 102.5743 | 103.4603
Chart: GtP + Heating demand 2040
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 192.9679 | 139.0027 | 123.932 | 61.8733 | 30.249 | 0 | 0 | 0 | 8.5175 | 49.3393 | 105.6512 | 154.2801
Gas to power | 115.6688 | 58.8793 | 33.3279 | 0 | 0 | 0 | 19.6682 | 24.5411 | 18.3174 | 15.3914 | 75.4256 | 87.9462
Chart: GtP + Heating demand 2030 (Slow HP)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 266.7677 | 192.1637 | 171.3292 | 85.5364 | 41.8176 | 0 | 0 | 0 | 11.775 | 68.209 | 146.057 | 213.2839
Gas to power | 108.8487 | 73.6747 | 63.805 | 39.9815 | 33.9559 | 45.8587 | 61.3189 | 60.8356 | 59.3265 | 58.6947 | 92.953 | 89.5625
Chart: GtP + Heating demand 2040 (Slow HP)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 220.0792 | 158.532 | 141.3439 | 70.5662 | 34.4989 | 0 | 0 | 0 | 9.7142 | 56.2713 | 120.4947 | 175.9558
Gas to power | 75.9793 | 30.396 | 7.5946 | 0 | 0 | 0 | 19.6682 | 24.5411 | 15.366 | 5.1122 | 51.5692 | 53.4861
Chart: GtP + Heating demand 2030 (Rapid HP)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 239.6565 | 172.6344 | 153.9173 | 76.8435 | 37.5677 | 0 | 0 | 0 | 10.5783 | 61.277 | 131.2134 | 191.6082
Gas to power | 151.5336 | 104.3077 | 91.4804 | 56.8852 | 41.7343 | 45.8587 | 61.3189 | 60.8356 | 62.5006 | 69.7497 | 118.6099 | 126.6233
Chart: GtP + Heating demand 2040 (Rapid HP)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 125.1899 | 90.1794 | 80.4021 | 40.1409 | 19.6243 | 0 | 0 | 0 | 5.5258 | 32.0094 | 68.5423 | 100.0908
Gas to power | 214.8925 | 130.0877 | 97.6612 | 37.9294 | 2.4598 | 0 | 19.6682 | 24.5411 | 25.6959 | 41.0896 | 135.0664 | 174.0963

## Slide 16
Insulation Sensitivity
Replacement + renovation+ p.a. (%) |  |  | 
Scenario | Slow | Base | Rapid
2022 | x | x | 
2030 | 1.6% (0.8/0.8) | 2.0% (1.0/1.0) | 2.7% (1.2/1.5)
 |  |  | 3.3% (1.2/2.1)
 |  | 2.5% (1.0/1.5) | 
2040 | 1.6% (0.8/0.8) |  | 
S/W swing in TWh |  |  | 
Scenario | Slow | Base | Rapid
2022 | 1,190 |  | 
2030 | 1,138 | 1,125 | 1,102
2040 | 1,039 | 989 | 933
Chart: GtP + Heating demand 2022
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 309.5262 | 222.9644 | 198.7905 | 99.2465 | 48.5203 | 0 | 0 | 0 | 13.6623 | 79.1417 | 169.4675 | 247.4698
Gas to power | 116.6394 | 97.1583 | 94.0379 | 74.8544 | 72.9859 | 81.1471 | 92.3268 | 87.1953 | 86.3242 | 93.2792 | 110.6221 | 107.4294
Chart: GtP + Heating demand 2030
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 256.601 | 184.8402 | 164.7997 | 82.2766 | 40.2239 | 0 | 0 | 0 | 11.3262 | 65.6095 | 140.4907 | 205.1555
Gas to power | 124.8556 | 85.1621 | 74.1833 | 46.3204 | 36.8728 | 45.8587 | 61.3189 | 60.8356 | 60.5168 | 62.8403 | 102.5743 | 103.4603
Chart: GtP + Heating demand 2040
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 192.9679 | 139.0027 | 123.932 | 61.8733 | 30.249 | 0 | 0 | 0 | 8.5175 | 49.3393 | 105.6512 | 154.2801
Gas to power | 115.6688 | 58.8793 | 33.3279 | 0 | 0 | 0 | 19.6682 | 24.5411 | 18.3174 | 15.3914 | 75.4256 | 87.9462
Chart: GtP + Heating demand 2030 (Slow Ins)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 260.4083 | 187.5827 | 167.2449 | 83.4973 | 40.8207 | 0 | 0 | 0 | 11.4943 | 66.5829 | 142.5751 | 208.1994
Gas to power | 124.8556 | 85.1621 | 74.1833 | 46.3204 | 36.8728 | 45.8587 | 61.3189 | 60.8356 | 60.5168 | 62.8403 | 102.5743 | 103.4603
Chart: GtP + Heating demand 2040 (Slow Ins)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 207.483 | 149.4585 | 133.2542 | 66.5274 | 32.5243 | 0 | 0 | 0 | 9.1582 | 53.0506 | 113.5983 | 165.8851
Gas to power | 115.6688 | 58.8793 | 33.3279 | 0 | 0 | 0 | 19.6682 | 24.5411 | 18.3174 | 15.3914 | 75.4256 | 87.9462
Chart: GtP + Heating demand 2030 (Rapid Ins)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 249.9384 | 180.0408 | 160.5207 | 80.1403 | 39.1795 | 0 | 0 | 0 | 11.0321 | 63.9059 | 136.8428 | 199.8286
Gas to power | 124.8556 | 85.1621 | 74.1833 | 46.3204 | 36.8728 | 45.8587 | 61.3189 | 60.8356 | 60.5168 | 62.8403 | 102.5743 | 103.4603
Chart: GtP + Heating demand 2040 (Rapid Ins)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 176.7872 | 127.3471 | 113.54 | 56.6851 | 27.7126 | 0 | 0 | 0 | 7.8033 | 45.2021 | 96.7921 | 141.3434
Gas to power | 115.6688 | 58.8793 | 33.3279 | 0 | 0 | 0 | 19.6682 | 24.5411 | 18.3174 | 15.3914 | 75.4256 | 87.9462

## Slide 17
EV sensitivity
EV in mil. units |  |  | 
Scenario | Slow | Base | Rapid
2022 |  | 6 | 
2030 | 25 | 35 | 50
2040 | 90 | 140 | 170
S/W swing in TWh |  |  | 
Scenario | Slow | Base | Rapid
2022 | 1,190 |  | 
2030 | 1,128 | 1,125 | 1,121
2040 | 940 | 989 | 995
Chart: GtP + Heating demand 2022
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 309.5262 | 222.9644 | 198.7905 | 99.2465 | 48.5203 | 0 | 0 | 0 | 13.6623 | 79.1417 | 169.4675 | 247.4698
Gas to power | 116.6394 | 97.1583 | 94.0379 | 74.8544 | 72.9859 | 81.1471 | 92.3268 | 87.1953 | 86.3242 | 93.2792 | 110.6221 | 107.4294
Chart: GtP + Heating demand 2030
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 256.601 | 184.8402 | 164.7997 | 82.2766 | 40.2239 | 0 | 0 | 0 | 11.3262 | 65.6095 | 140.4907 | 205.1555
Gas to power | 124.8556 | 85.1621 | 74.1833 | 46.3204 | 36.8728 | 45.8587 | 61.3189 | 60.8356 | 60.5168 | 62.8403 | 102.5743 | 103.4603
Chart: GtP + Heating demand 2040
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 192.9679 | 139.0027 | 123.932 | 61.8733 | 30.249 | 0 | 0 | 0 | 8.5175 | 49.3393 | 105.6512 | 154.2801
Gas to power | 115.6688 | 58.8793 | 33.3279 | 0 | 0 | 0 | 19.6682 | 24.5411 | 18.3174 | 15.3914 | 75.4256 | 87.9462
Chart: GtP + Heating demand 2030 (Slow EV)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 256.601 | 184.8402 | 164.7997 | 82.2766 | 40.2239 | 0 | 0 | 0 | 11.3262 | 65.6095 | 140.4907 | 205.1555
Gas to power | 120.5536 | 80.917 | 70.5181 | 42.8615 | 32.9779 | 41.1909 | 55.7523 | 55.2076 | 56.1404 | 58.4975 | 98.9554 | 98.7778
Chart: GtP + Heating demand 2040 (Slow EV)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 192.9679 | 139.0027 | 123.932 | 61.8733 | 30.249 | 0 | 0 | 0 | 8.5175 | 49.3393 | 105.6512 | 154.2801
Gas to power | 95.6686 | 39.1435 | 16.2879 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 58.6005 | 66.1767
Chart: GtP + Heating demand 2030 (Rapid EV)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 256.601 | 184.8402 | 164.7997 | 82.2766 | 40.2239 | 0 | 0 | 0 | 11.3262 | 65.6095 | 140.4907 | 205.1555
Gas to power | 131.3085 | 91.5297 | 79.6811 | 51.5087 | 42.7153 | 52.8604 | 69.6687 | 69.2777 | 67.0813 | 69.3545 | 108.0028 | 110.484
Chart: GtP + Heating demand 2040 (Rapid EV)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Heating | 192.9679 | 139.0027 | 123.932 | 61.8733 | 30.249 | 0 | 0 | 0 | 8.5175 | 49.3393 | 105.6512 | 154.2801
Gas to power | 127.6689 | 70.7209 | 43.5519 | 8.2841 | 0 | 11.0501 | 35.1959 | 40.2405 | 30.5251 | 27.5055 | 85.5206 | 101.0079

## Slide 18
Gas for Space Heating
Space heating demand
There are fundamentally three ways how space heating demand for gas will decrease in the years to come:
  Fuel switching to HP
  Better insulation
  Climate and behavioral changes - not reflected yet [TO DO]
The overall effect on seasonal demand will be a decline by 17.1% by 2030 and 37.7% by 2040
Fuel switching to HP
Increased penetration of HPs will pressure gas market share from 44% (2022) to 37% in 2030 and 34% in 2040 (we assume HPs will be replacing all the other sources proportionally)
[TO DO: prioritise oil/coal to HP switching]
Better insulation
Annually 2.0% or 2.5% (up to vs. after 2030) of building stock will be newly built or newly renovated, resulting into 36% and 61% of buildings well insulated in 2030 and 2040 respectively (up from 20% in 2022)
Great part of these replacements / renovations will be connected with HP installation, thus the overall effect will be combined
[TO DO: allocate gas demand replacement to various factors]
Chart: Change in seasonal demand
| 2022 | 2030 | 2040
Seasonal demand | 1388.7894 | 1151.3233 | 865.813
Gas demand replaced | 237.4661 | 522.9764
Total | 1388.7894 | 1415.8396 | 1427.8541

## Slide 19
Scenarios for power generation: assumptions & Annual
Scenario | Actual (2022) | Equinor (Walls) | IEA (Stated policies) | Ember (Stated policies)
Power demand in TWh (2030/2040) | 2,777 | 3,043 / 3,268 | 3,256 / n.a. | 3,000 / 4,359
Wind+Solar share (2030/2040) | 23% | 34% / 48% | 49% / n.a. | 47% / 72%
CO2 emissions reduction (1990 vs 2022 or 2050) | 27% | 81% | 76% | 100%
We present here three scenarios for power generation
Equinor (Walls) fits the best given the current trajectory of renewables
RePowerEU target for wind+solar share in 2030 is 55%
Chart: Gas to power scenarios (Eq-Walls)
| 2022 | ... | Slow | Base | Rapid | ... | Slow | Base | Rapid
Gas to power | 1114 | 736.3667 | 864.7991 | 1070.207 | 133.1 | 449.166 | 1047.5228
Chart: Solar power generation
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | Eq-Walls | IEA-St.pol. | Ember-St.pol. | RePowerEU | WoodMac | Eq-Walls | Ember-St.pol.
Solar | 107.3 | 113.79 | 124.54 | 144.82 | 163.14 | 210.75 | 247.06 | 310 | 626 | 449.7796 | 563.8494 | 514.9824 | 484 | 1095.8785
CAGR line 17-23 Solar | 477.89 | 617.65
CAGR: 14,9% | 547.77
CAGR line 23-30 Solar | 557.06 | 620
CAGR: 3,3% | 588.53
CAGR line 30-40 Solar | 36.0304 | 210.0304
CAGR: 4,6% | 123.0304
Chart: Wind power generation
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | Eq-Walls | IEA-St.pol. | Ember-St.pol. | RePowerEU | WoodMac | Eq-Walls | Ember-St.pol.
Wind | 312.3 | 320.62 | 367.13 | 397.78 | 386.84 | 419.95 | 470.65 | 730 | 985 | 957.217 | 1025.6978 | 779.9577 | 1100 | 2029.4834
CAGR line 17-23 Wind | 782.95 | 941.3
CAGR: 7,1% | 862.125
CAGR line 23-30 Wind | 1200.65 | 1460
CAGR: 6,5% | 1330.325
CAGR line 30-40 Wind | 1379.4347 | 1749.4347
CAGR: 4,2% | 1564.4347

## Slide 20
Sensitivity scenarios (using Walls for power generation)
We model three scenarios in the sensitivity analysis (Base scenario was described so far in the presentation)
In all of them Equinor (Walls) is used for power generation segment
Scenario | 2022 | Slow | Base | Rapid
HP in mil. units (2030/2040) | 20 | 34 / 44 | 40 / 60 | 50 / 100
Replacement + renovation p.a. (%) (2030/2040) |  | 1.6%/1.6% | 2%/2.5% | 2.7%/3.3%
of which (insulation/replacement) |  | (0.8/0.8) | (1/1)/(1/1.5) | (1.2/1.5)/(1.2/2.1)
EV in mil. units (2030/2040) | 6 | 25/90 | 35/140 | 50/170
Chart: Seasonal demand scenarios (Eq-Walls)
| 2022 | ... | Slow | Base | Rapid | ... | Slow | Base | Rapid
Heating | 1388.7894 | 1214.0219 | 1151.3233 | 1045.4021 | 1052.5829 | 865.813 | 489.1047
Chart: Gas to power scenarios (Eq-Walls)
| 2022 | ... | Slow | Base | Rapid | ... | Slow | Base | Rapid
Gas to power | 1114 | 736.3667 | 864.7991 | 1070.207 | 133.1 | 449.166 | 1047.5228
Chart: Power generation
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | Eq-Walls | IEA-St.pol. | Ember-St.pol. | Eq-Walls | Ember-St.pol.
PG | 2923.53 | 2908.18 | 2874.55 | 2752.86 | 2874.98 | 2777.03 | 2694.69 | 3043 | 3256 | 2999.5487 | 3268 | 4358.5033
CAGR line 17-23 PG | 4092.942 | 3864.102
CAGR: -1,3% | 3978.522
CAGR line 23-30 PG | 4216.19 | 4564.5
CAGR: 1,8% | 4390.345
CAGR line 30-40 PG | 863.7483 | 1088.7483
CAGR: 0,7% | 976.2483

## Slide 21
Daily variability of gas demand

## Slide 22
Backup
Scenarios to 2030 | 2022 | Fit for 55 | RePowerEU | Base
HP in mil. units 2030 | 20 | 40 | 41.5 | 40
of which (medium&deep renovation) | <0.8% | 1.9% | 2.1% | 0.8%
Installed wind capacity in GW | 204 | 469 | 510 | 342
Installed solar PV capacity in GW | 207 | 530 | 592 | 330
Chart: Solar capacity
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | FF55 | RePowerEU | Our Base
Installed solar PV capacity in GW | 97 | 104 | 121 | 139 | 165 | 207 | 262.9 | 530 | 592 | 329.8753
CAGR line 17-23 Solar cap | 307.32 | 473.22
CAGR: 18,1% | 390.27
CAGR line 23-30 Solar FF55 | 421.9 | 689
CAGR: 10,5% | 555.45
CAGR line 23-30 Solar RePEU | 558.9 | 888
CAGR: 12,3% | 723.45
CAGR line 23-30 Solar Our Base | 15.4935 | 82.4688
CAGR: 3,3% | 48.9812
Chart: Wind capacity
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | FF55 | RePowerEU | Our Base
Installed wind capacity in GW | 148.9123 | 157.2115 | 167.1391 | 177.0588 | 188.3708 | 204.499 | 220.252 | 469 | 510 | 341.6211
1 7 | 325.1139 | 396.4536
CAGR: 6,7% | 360.7837
CAGR line 23-30 Wind FF55 | 360.952 | 609.7
CAGR: 11,4% | 485.326
CAGR line 23-30 Wind RePEU | 454.752 | 744.5
CAGR: 12,7% | 599.626
CAGR line 23-30 Wind Our Base | 49.4415 | 170.8105
CAGR: 6,5% | 110.126
Chart: Replacement & renovation rate
| 2023 | FF55 | RePowerEU | Our Base
Annual renovation rate of which (medium&deep renovation) | 0.008 | 0.019 | 0.021 | 0.008
CAGR line 23-30 Insulation FF55 | 0.0137 | 0.0247
CAGR: 13,2% | 0.0192
CAGR line 23-30 Insulation RePEU | 0.025103 | 0.038103
CAGR: 14,8% | 0.031603
CAGR line 23-30 Insulation Our Base | 0.036505 | 0.036505
CAGR: 0,0% | 0.036505

## Slide 23
BACKUP
Electric vehicles (EVs)
2022: 6 mil. Evs (https://alternative-fuels-observatory.ec.europa.eu/transport-mode/road/european-union-eu27)
2030: 35 mil. Evs (More specifically, EU road passenger transport must reach 30m electric vehicles by 2030, close to six times more than the 5.3m registered today https://www.rabobank.com/knowledge/d011340306-the-takeoff-of-the-passenger-electric-vehicle-market-a-pathway-toward-the-eus-2030-e-mobility-targets, https://www.consultancy.eu/news/5766/europes-electric-vehicles-fleet-to-reach-40-million-by-2030)
2040: 140 mil. Evs (https://www.iea.org/data-and-statistics/charts/global-ev-stock-by-mode-in-the-sustainable-development-scenario-2020-2030, https://www.iea.org/data-and-statistics/charts/electric-vehicle-fleet-in-2040-in-the-future-is-electric-and-new-policies-scenarios , The deployment of electric vehicles (EVs) is expected to quadruple over 2031-2040 (GIE))
Avg. consumption: 0.2 kWh/km (https://ev-database.org/cheatsheet/energy-consumption-electric-car)
Annual mileage: 11,300 km/car (2022) +23% in 2030/2040) (Change in distance travelled by car | ODYSSEE-MURE , https://ev-database.org/cheatsheet/energy-consumption-electric-car)
Kms peak in Sum, battery drain in Win (Range test: How far can electric cars go in winter? | What Car?)

## Slide 24
backup
Heat pumps (HPs)
2022: 20 mil. HPs (90% used for space heating, EHPA market report 2023)
2030/2040: 40/50 mil. (RePowerEU & Fit for 55, 90% used for space heating, ATMO 2022)
Insulation
replacement rate of 1% p.a. (https://www.knaufinsulation.com/news/insulating-all-europes-residential-buildings-can-cut-energy-demand-for-space-heating-by-44)
Insulation rate of 0,8% p.a. (1% of 136 mil. (not insulated buildings)) How-to-stay-warm-and-save-energy_final-report(2).pdf
Savings via insulation: 32% (avg. Calc. From Measuring the Returns to Home Insulation and BPIE)
Building stock
131 mil. buildings in EU (119/12) https://www.rics.org/news-insights/energy-efficiency-of-the-building-stock-in-the-eu
3:1 in square meters (EC Technical reports)